L-BAND OPTICAL FIBER OPTICAL SOURCE

1. Information of the patent

| Dowon International Administration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Registration 11 | 10-580610 | 2003-52575 | Korea Institute of Industrial Technology | G02B 6/10 |
| Registration 11 | 2006.05.09 | 2003.07.30 | Korea Institute of Industrial Technology | G02B 6/10 |
| Representative fig. |

2. Summary of the technology

This technology relates to an L-band(Long wavelength-band) optical fiber optical source to raise radiating efficiency amplifying power of an L-band natural light.

As this technology relates to an L-band optical fiber, there have been problems that an L-band(Long wavelength-band) natural light's efficiency, unlike the C-band(Conventional-band) natural light using high inversion state, is decreased by using the inversion state, and the L-band natural light has to use the expensive and 4~8 times longer EDF(EDF-Erbium Doped Fiber) amplifier to raise the power of an L-band.  Therefore, there have been many proposals to raise an L-band natural light's efficiency, but it has a disadvantage of high price because of its low efficiency and need of additional EDF.

As in the development of an amplified L-band optical fiber optical source that is essential for raise the capacity of communication, a primary object of this technology is to provide L-band erbium added optical fiber optical source, which can raise the pumping efficiency in the long wavelength band. And, also it is a devised technology to provided a trust raised erbium-added optical fiber optical source without using expensive non-pumping EDF(Erbium-Doped Fiber) structure by replacing a passive element for reduce the price.

This technology, related to an L-band optical fiber optical source for raise the efficiency of the emitting light, is comprised of an erbium-added optical fiber amplifier pumped with a pumping light, an isolator that prevents from moving to opposite direction installed in the latter part of the afore said erbium-added optical fiber amplifier therein, a wavelength division multiplexer that receives a pumping source installed in the previous part of the afore said erbium-added optical fiber amplifier, a wavelength selective mixer that divides a amplified spontaneous emission into an L-band(Long wavelength-band) and a C-band(Conventional-band) in an erbium-added optical fiber amplifier, a reflector that reflects the L-band light installed in the previous part of the afore said wavelength selective mixer, and an FBG(Fiber Bragg Grating) that selectively reflects the C-band light.

3. Special features and/or characteristics of the technology

According to this technology, it is characterized in that the wasted optical light can be used effectively by selectively reflecting the part of the C-band of amplified spontaneous emission separated from the first wavelength selective mixer by the FBG(Fiber Bragg Grating), and by utilizing the remained natural light as a second excitation light to be incident into the second wavelength selective mixer and to be incident into the end portion of the EDF.

This technology also has features that it can provide an erbium-added L-band optical fiber optical source that can raise the efficiency of the amplifying by comprising a wavelength selective mixer, a reflector and L-band natural light source of the FBG, and can provide erbium-added L-band optical fiber optical source with the reduced price and raised trust by amplifying the power of the natural generated light of the L-band without using the expensive non-pumping EDF(Erbium-Doped Fiber).

4. Applicable market and use of the technology

An optical fiber roughly can be used for communication, image transmission, and a detector. An optical fiber for communication is divided into for general communication network, like the use of home and industry and for the communication medium, like cable and television. In this case, cord or cable can be made and used by the method of the outer cover being covered on the first cover of an optical fiber. The optical fiber for image transmission is used for medical endoscope made of a bundle of short-length optical fiber or for an image amplifier to see the inner portion of the narrow and winding parts. An optical fiber for a detector is used single mode optical fiber, in this case, it is used the point that the afore said optical fiber is sensitive to the outer change, for example, pressure, temperature, speed, and magnetic flux to thereby it can be used for a gyroscope, a detector of high voltage electric current, and an underwater sonar.

This technology, related to an optical fiber, not only can be applicable to a market that deals with the hybrid fiber coax used by the CATE network, but also to a market that deals with industrial laser or medical laser.