3D DRAWING CONFERENCING METHOD EMPLOYING PDA

1. Information of the patent

| Dowon International Administration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Application 61 | - | 2006-117544 | Korea Institute of Industrial Technology | H04B 1/40 |
| Application 61 | - | 2006.11.27 | Korea Institute of Industrial Technology | H04B 1/40 |
| Representative Fig. |

2. Summary of the technology

ㅇ	This technology relates to a real-time 3D drawing conferencing method employing a PDA(Personal Digital Assistant).

ㅇ	A PDA, having a low data processing capability when compared with desktop computers or notebook computers, had a lot of difficulties in transmitting and processing files and was problematic in that it could not perform smooth conferencing.  Further, the PDA had a problem in that smooth access was difficult due to the overload of a main server when there were lots of workers.

This technology is a technology that has been developed to solve the above problems so that workers at different places can exchange their opinions smoothly while confirming the same 3D drawing using a PDA.  That is, this technology is an improved technology, which can provide a real-time 3D drawing conferencing method employing a PDA and can reduce the load of a main server.

ㅇ	This technology is a technology regarding a real-time 3D drawing conferencing method employing a PDA, in which workers at different places can exchange their opinions about the same drawing using any one of PDAs equipped with local area radio communication means.  The real-time 3D drawing conferencing method includes the steps of (S1) allowing the workers to select any one of their PDAs, specify the selected PDA as a center PDA, and request a 3D drawing for which exchange of opinions is required from a main server through the center PDA; (S2) allowing the main server to convert the 3D drawing file, which has been requested in the step (S1), into a file having design information, measurement information, analysis information and design/conference information; (S3) allowing the main server to transmit the file, which has been converted in the step (S2), to the center PDA and allowing the center PDA to convert the received file into an image file; and (S4) allowing the center PDA to transmit the image file, which has been generated in the center PDA through the step (S3), to remaining local PDAs so that the workers can exchange their opinions while sharing the 3D drawing.

3. Characteristics and/or advantages of the technology

In this technology, the center PDA is connected to the main server, and functions to assist the main server and serves as a temporary server, thereby reducing the load of the main server.  The remaining local PDAs serve as monitors for displaying the image file transmitted from the center PDA.  Accordingly, there is an advantage in that workers at different places can exchange their opinions while sharing the same 3D drawing.

This technology has advantages in that it can reduce the size of a 3D drawing file and thus smoothly perform the conferencing of a drawing employing a PDA.  Further, this technology is advantageous in that when the number of workers who share a drawing is small, a center PDA is designated and serves as a temporary server, so that the load of a main server can be reduced and smooth conferencing is possible.

A file of a format that has been newly presented by this technology further includes analysis information and measurement information.  Thus, when converting the file into an image file, an image similar to a real 3D drawing can be created.  Due to this, local PDA users can expect the same effects as seeing a real 3D drawing.  Further, there is an advantage in that it can confirm an image file using only a basis utility program included in a PDA even without installing a dedicated program.

4. Applicable market and use of the technology

This technology relates to a conferencing method employing a PDA.  The PDA is a small-sized computer much smaller than a notebook, and provides functions such as address book, a memo note and simple document check.  The PDA has a very wide range of applications such as free exchange of data through connection with a PC.  In recent years, with the development of a radio communication technology, data has become exchanged with other PDA located at a local area through access to an Internet using a PDA, or local area radio communication means such as Bluetooth.  With the development of PDA related technologies, a PDA has been used for various purposes in various industries as well as the limited use ranges such as diary management, address book and memo note.  Through the introduction of a PDA, various check results can be input on the spot and the input check results can be input to a main server through wireless Internet or a local area radio communication means, thereby improving workability.  Further, if exchange of opinions about a product between workers at different places is required even within the same spot, the workers can exchange their opinions while exchanging various drawings and data of the product through local area radio communication means.  Thus, a system with improved productivity and quality can be constructed.  The PDA can use an Internet, such as search of web pages, transmission and reception of e-mail, PC communication and stock trading, in addition to an electronic scheduler through connection to a mobile phone while moving irrespective of places.

Further, the PDA can provide personal information management programs for a PC, add input information and support backup through connection to a PC.  Thus, business efficiency of a specific field, such as sales management, vehicle, transportation and stock management, as well as the frame of personal information management, can be maximized.

This PDA is a technology that can be used in several sectors of a modern society, and it is considered that the application of this technology is infinite.