APPARATUS AND METHOD FOR EXPRESSING EMOTION OF ANDROID ROBOT

1. Information of the patent

| Dowon International Administration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Application 75 | - | 2006-130636 | Korea Institute of Industrial Technology | B25J 17/02 |
| Application 75 | - | 2006.12.20 | Korea Institute of Industrial Technology | B25J 17/02 |
| Representative Fig. |

2. Summary of the technology

ㅇ	This technology relates to an apparatus and method for expressing emotions of an Android robot.

ㅇ	A conventional robot had a limited behavior although it was delicate and was not practical.  Further, the conventional robot could recognize signals from a human, but had a difficulty in providing signals.  This technology is a technology for solving the problems is an improved technology having an object to provide an apparatus and method, which can express emotion states of an Android robot having a skin and movement similar to that of a human as a skin and joint structure similar to a human and can express emotions to a counterpart using vision, voice and texts, so more friendly communication with a human can be performed, the demand for new technologies related to robots can be increased, and acceleration of the robot market can be contributed.

ㅇ	This technology relates to an apparatus and method for expressing emotions of an Android robot, and includes a vision unit for extracting facial expressions, colors and motion of a human, which are photographed through a camera and emotional information of a human through recognition of an object an intelligence unit for extracting a human’s voice input through a microphone, personalities detected through data provided from the vision unit, and emotional information from emotion models and texts, and selecting and managing emotion to be expressed by a robot through a database in which facial expressions and gestures edited according to motors applied to respective axes; and a motion controller for executing emotional behaviors by employing data transmitted from the vision unit and the intelligence unit and mediating the motors of the respective axes to perform desired operations in a scenario unit.

3. Characteristics and/or advantages of the technology

This technology is characterized in that it includes a vision processing step of extracting emotional information of a human by employing an image signal captured by the camera, an intelligence processing step of extracting emotional information by employing motion information extracted by the image signal captured through the camera, a sound signal input through a microphone, and a text signal input through a web, messenger or a keyboard and editing the emotional information according to the motors applied to respective axes; and a motion control step of controlling motor driving of each part of a robot according to a signal that is extracted, edited and output from the intelligence processing step.

In this technology, an Android robot can express emotion states as a skin and joint structure similar to that of a human and express emotion to a counterpart through vision, voice or texts.  Accordingly, this technology is advantageous in that it can perform more friendly communication with a human, increase the demand for new technologies related to robots, and contribute to the acceleration of the robot market.

4. Applicable market and use of the technology

This technology is a technology regarding an apparatus and method for expressing emotion of an Android robot.  Android refers to a robot that looks like a human and behaves similar to a human or an intelligent life thereof and is a name referring to an artificial human appearing in an imaginary scientific novel, etc.  This Android robot can be applicable to all fields of a human society since it has a similar shape as that of a human.  Further, in a modern society becoming a nuclear family, the Android robot can be used as a constituent member of a family, can be used for medical treatment, military affairs, industry, universe, deep sea probe, and so on.  It can also be said that application fields of the Android robot is further expanded.