METHOD OF TESTING PHYSICAL STRENGTH THROUGH BIO SIGNAL MEASUREMENT; and APPARATUS FOR MEASURING BIO SIGNAL AND METHOD OF TESTING PHYSICAL STRENGTH EMPLOYING THE SAME

1. Information of the patent

| Dowon International Administration Nos. | Registration Nos. | Application Nos. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration Nos. | Date of registration | Date of filing | Rightful institution | Remarks |
| Application 94 | - | 2006-75929 | Korea Institute of Industrial Technology | A61B 5/02 |
| Application 94 | - | 2006.08.11 | Korea Institute of Industrial Technology | A61B 5/02 |
| Application 95 | - | 2007-58674 | Korea Institute of Industrial Technology | A61B 5/02 |
| Application 95 | - | 2006.06.15 | Korea Institute of Industrial Technology | A61B 5/02 |
| Application 96 | - | 2007-76173 | Korea Institute of Industrial Technology | A61B 5/02 |
| Application 96 | - | 2007.07.30 | Korea Institute of Industrial Technology | A61B 5/02 |
| Representative Figs. |

2. Summary of the technology

ㅇ 	This technology relates to I) a method of testing physical strength by measuring the heart rate before and after a user’s exercise; and II)　an apparatus for a bio signal test for prescription on the basis of a physical strength test value of a tester through the heart rate test during exercise.  This technology also relates to an apparatus for a bio signal test and a physical strength test method employing the same.

ㅇ 	This technology is I) a technology that has improved a disadvantage in which accuracy is very low in a student physical strength test of conventional physical strength test technologies; a disadvantage in which an exercise load test is an accurate test method using various expensive equipments, but has low economy and a complicated test method a disadvantage in which a basic physical strength test requires more expensive apparatus than that of an exercise load test and more test expenses and test time and has low economy and a complicated test method; a significant disadvantage in which the whole body endurance test method has a significant problem in safety, which is caused by physical and psychological loads, and has a severe deviation per on an individual with respect to power, and so on; and II) an improved technology that has improved a problem in which an accurate test is not performed since a test time is not accurate, a problem in which a fabrication cost is increased because an additional circuit for detecting whether the hands touch a hand electrode in order to obviate delay depending on a time gap, a problem in which an accurate test is not performed since conditions, such as a grip position or pressure in the repetitive process of gripping the hand electrode after the button is manipulated, a problem in which a signal is varied according to the pressure of a tester who grips the hand electrode, in particular, a distorted test signal is output if the pressure is changed during the test, and an accurate test is not performed, a problem in which it is difficult to decide a load at a specific point of time, and so on; and III) a technology of an apparatus for a bio signal test for testing a physical strength state for exercise prescription of a user by testing the heart rate through exercise according to a preset protocol, including a test panel; a test unit provided in the test panel and configured to test the heart rate for exercise prescription through touch of the palm; a display unit provided in the test panel and configured to display the test value of the heart rate and display information,  including a value of a body ability value for exercise prescription which is calculated through the test value a button unit disposed at a location where the thumb can touch in a state where the palm of a human body has touched the test unit and configured to actuate the apparatus for a bio signal test and a controller for calculating an adequate body ability value for exercise prescription through the heart rate test value of the human body tested by the test unit and classifying/inducing a level value according to exercise prescription based on the body ability value.

ㅇ	This technology is I) a technology including the steps of inputting information of a user through an input unit of a physical strength test apparatus primarily testing a stable state heart rate before the user’s exercise through a heart rate test unit; allowing the user to exercise as much as a set amount according to repeated signal sounds of the physical strength test apparatus based on the start of the exercise after the primary test of the heart rate of the user; secondarily testing the heart rate after the user’s exercise is finished through the heart rate test unit; allowing the user to take a rest for a predetermined time according to a signal sound of the physical strength test apparatus after the secondary test of the heart rate of the user; thirdly testing the user’s heart rate through the heart rate test unit after the user has taken a rest for a predetermined time; calculating a slope of the first, second and third heart rate stored test values; comparing the slope values of the first, second and third test heart rates and data values of previously stored physical strength information; and displaying the resulting value of a user physical strength state, which is obtained through comparison with the previously stored physical strength information data value, on a display unit; and II) a technology of an apparatus for a bio signal test for testing a physical strength state for exercise prescription of a user by testing the heart rate through exercise according to a preset protocol, including a test panel; a test unit provided in the test panel and configured to test the heart rate for exercise prescription through touch of the palm; a display unit provided in the test panel and configured to display the test value of the heart rate and display information,  including a value of a body ability value for exercise prescription which is calculated through the test value a button unit disposed at a location where the thumb can touch in a state where the palm of a human body has touched the test unit and configured to actuate the apparatus for a bio signal test and a controller for calculating an adequate body ability value for exercise prescription through the heart rate test value of the human body tested by the test unit and classifying/inducing a level value according to exercise prescription based on the body ability value.

3. Characteristics and/or advantages of the technology

This technology is advantageous in that I) it is simpler than the existing technology by using the physical strength test apparatus and can execute the physical strength test of a user for a short period of time.  That is, since a difficulty index of an exercise state and exercise is low, psychological load of an excessive exercise can be freed.  Accordingly, the apparatus of this technology can be used without load over the whole age groups and is advantageous in that it can significantly lower physical/psychological stress; and advantageous in that II) it can obviate time delay between a button input and a test start because the operation of the button unit for a heart rate testis performed with the hand touched thereto and save the production cost of a product since an additional circuit for preventing time delay between a button input and a test start.  Further, this technology is advantageous in that a user can be provided with a user interface which enables an easy operation of the button for actuating the apparatus and selecting a function since the number of an input button and a select button is reduced to four.  Further, III) in accordance with the physical strength test method employing the apparatus for a bio signal test according to this technology, a bio signal is tested using a method of testing load in a target heart rate region through monitoring a varying heart rate of a tester.  Accordingly, there is an advantage in that an exercise level for an adequate exercise prescription according to a tester’s physical ability can be decided.

4. Applicable market and use of the technology

This technology is I) a technology regarding a physical strength measurement method, and it can be utilized in a student physical strength test, an exercise load test, a basic physical strength test, the whole body endurance test and so on and can be used in the fields of exercise devices, health care medical devices, and medicines such as health exercise apparatuses and physical strength test apparatus; and II) a technology regarding a heart rate test apparatus that can be attached to a health exercise device, and it can be attached to exercise devices such as health exercise equipment and physical strength test device.  Further, this technology can be used in various ways in the fields of health care medical devices and medicines since an exercise level for a user’s exercise prescription can be decided.