ROBOT FOR BRIDGE SAFETY PROBE

1. Information of the patent

| Dowon International Administration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Application 33 | - | 2006-91031 | Korea Institute of Industrial Technology | G01N 21/88 |
| Application 33 | - | 2006.09.20 | Korea Institute of Industrial Technology | G01N 21/88 |
| Representative Fig. |

2. Summary of the technology

ㅇ	This technology relates to a robot for bridge safety probe which can accurately inspect the safety of a lower portion of a bridge sole plate through equipment mounted for safety check while flying semi-automatically or automatically through a flight probe robot in which a flight robot and a moving robot are integrated into one and moving through the traveling of the moving robot in a state where the robot for bridge safety probe is attached to the lower portion of the bridge sole plate.

ㅇ	A method and apparatus for inspecting defects of a bridge employing a conventional vision system could secure the work efficiency and safety, but was problematic in that it still required many apparatus.  Further, the conventional method and apparatus, as a method according to the movement of a mounted inspection vehicle, had a problem in that the work range was limited and inconvenient.

This technology is an improved technology that is able to accurately inspect the safety of a lower portion of a bridge sole plate by employing the flight probe robot which performs both flight and traveling.

ㅇ	This technology relates to a robot for bridge safety probe, comprising a flight probe robot including a flight robot coupled to a main body housing and equipped with a driver for generating thrust necessary for semi-automatic or automatic flight, a moving robot coupled to the main body housing and configured to travel with it attached to a lower portion of a bridge sole plate through thrust and hovering of the flight robot, a navigation sensor module for sensing the flight state of the flight robot, a camera module for capturing an image of the lower portion of the bridge sole plate and providing the captured image, a communication module for performing communication with a ground control module, and a control module for controlling flight and traveling of the flight robot and the moving robot based on various control signals of the ground control module, which are received through the communication module and the ground control module for transmitting various control signals necessary for flight and operation of the flight robot and the moving robot of the flight probe robot and displaying the image of the lower portion of the bridge sole plate, which is received from the camera module of the flight probe robot.

3. Characteristics and/or advantages of the technology

This technology is characterized in that it can inspect the safety of a lower portion of a sole plate of a bridge accurately by attaching the moving robot to the lower portion of the bridge sole plate through thrust of the flight robot, capturing an image of the lower portion of the bridge sole plate through the mounted camera while the moving robot attached to the lower portion of the bridge sole plate, and providing the captured image.

This technology features that it has a wide range of work, does not require lots of equipments, and can increase work efficiency, safety and convenience.

4. Applicable market and use of the technology

This technology can be applied to perform external inspection of an underlying structure of a bridge, which is difficult for periodic eye inspection, when performing external inspection in order to the degree of aging of large-sized structures such as bridges.  That is, this technology can be applied to inspect cracks or corrosion of structures by carrying out safety check and diagnosis into industrial nucleus facilities periodically so as to secure the safety of the facilities such as bridges.

This technology can also be widely used to perform external inspection of specific structure, such as dams or tunnels which cannot be inspected directly by humans, as well as bridges.