A WATER COOLING TYPE COOLER FOR A SEMICONDUCTOR DEVICE

1. Information of the patent

| Dowon International Administration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Application 6 | - | 2007-19505 | Korea Institute of Industrial Technology | H05K 7/20 |
| Application 6 | - | 2007.02.27 | Korea Institute of Industrial Technology | H05K 7/20 |
| Representative Fig. |

2. Summary of the technology

This technology relates to a water cooling type cooler for a semiconductor device that can effectively cool the heat generated during the operation of an information processing terminal like a computer and can have an integrated configuration, thereby allowing the installation area to be reduced and also allowing the installation to be easy.

In conventional practices, there are defects in that there is a limitation in increasing the number of heat sink fins so as to enlarge the surface area of heat exchange of a heat sink and the cooling efficiency is low, and thus, according to this technology the cooler is installed at a relatively small space and the heat sink has a plurality of heat sink fins.

According to this technology, there is disclosed a water cooling type cooler for a semiconductor device comprising: a water block mounted at one side of the semiconductor device; a reservoir for receiving refrigerants being ejected in heat-exchanged states from the water block therein; a radiator for receiving the refrigerants radiated from the reservoir therein; a pump for supplying the circulated and radiated refrigerants in the radiator to the water block again; and a blower fan for blowing the refrigerants to the radiator and the reservoir.

3. Characteristics and/or advantages of the technology

According to this technology, the cooler is directly contacted with the semiconductor device such that the refrigerants in the water block absorbing the heat generated from the semiconductor device are distributed and conveyed to the parts having radiating functions, thereby reducing the load of the pump supplying the refrigerants to the water block and thereby improving the cooling performance thereof.

According to this technology, the refrigerants that are heat-exchanged in the water block are radiated to two steps by means of the reservoir and the radiator, thereby increasing the cooling efficiency thereof, and further, the respective parts are assembled integrally with each other in a serial relation with each other to reduce the entire size, thereby reducing the installation area and allowing the installation to be easy.

4. Applicable market and use of the technology

This technology relates to a cooler for a computer, an information processing terminal and a semiconductor device, such that it can be applied to cooler-producing companies and to a variety of products in computer and information communication fields.