MEASUREMENT SYSTEM USING DIODE LASER

1. Information of the patent

| Dowon International Administration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Registration 24 | 10-551232 | 2003-2164 | Korea Institute of Industrial Technology | G01N 15/14 |
| Registration 24 | 2006.02.03 | 2003.01.13 | Korea Institute of Industrial Technology | G01N 15/14 |
| Representative Fig. |

2. Summary of the technology

This technology relates to a measurement system using a diode laser that can measure required information by non-contact method without any affection to air fluids and flames.

A measurement system is a highly important apparatus that analyzes and researches the object matter so that it can be a basis for research and development to solve the object matter's problems.

Generally, there are contact and non-contact measurement systems to understand the object matter's characteristics, and with the regard to them, each of the problems have been overcome according to this technology. That is, this technology can not only to provide the exact required information by using the information from fluids and flames by projecting beams to fluids or flames but also is devised technology of trust raised with regard to measurement result because it doesn't generate any harmful thing during the laser beams projected to fluids or flames.

A measurement system of this technology using a diode laser is comprised of a radiating part including a plurality of diode laser emitting beam with a specific wavelength a photo detecting part detecting and changing the laser beam to electrical signals for detecting the intensity of radiation absorbed by medium during the radiated laser beams from the aforesaid plurality of diode laser passing through a medium a collecting and analysis part collecting the electrical signals generated from the aforesaid photo detecting part and analyzing the electrical signals for classifying the emitted laser beams form the aforesaid plurality of diode laser a control part controlling the aforesaid diode laser's temperature and electrical current injected to the diode laser for control the wavelength of emitted laser beam a signal generating part, which is connected to the aforesaid collecting and analysis part, changing the wavelength of laser beams passing through the medium by adding the intrinsic electrical signals having respectively different forms with the aforesaid diode lasers to the collecting and analysis part for classifying the laser beams of the aforesaid collecting and analysis part and a central processing unit, which is connected to the aforesaid signal generating part and the control part, processing data and controlling the aforesaid signal generating part.

3. Characteristics and/or advantages of the technology

This technology characterized in that it is lower price and is easier to treat than the conventional measurement system of fluids and flames.

This technology also features that it can exactly measure required information of each element's concentration, temperature, speed of a running fluid, and mass flux by the non-contact method without any affection to fluids and flames.

In addition, this technology has an advantage in that it is possible to use this technology in the construction field like in the developed countries. That is, a gas generated from when concrete or reinforcing rod are corroded in the inner side of a construction that is impossible to be measured by naked eye can be measured exactly by non-destruction or non-contact method.

4. Applicable market and use of the technology

This technology can be applicable technology to anyplace where needs to burn fuel, for examples, home, business place, or factory that need to have a gas leakage detector, and also industrial world having a trash burner. And it is a useful technology for manufacturing industry of a gas leakage detector or measurement system used for industrial world having a trash burner. Recently, the applicable coverage can be extended to construction industry, for example, when a structure or a facility's inner side of that is impossible to be checked by naked eye can be measured by the non-destruction and non-contact method during or after the construction.