HEAT SINK HAVING HEAT PIPE FUNCTION; and METHOD FOR MANUFACTURING A HEAT SINK HAVING THERMAL SIPHON FUNCTION

1. Information of the patent

| Dowon International Administration Nos. | Publication Nos. | Application Nos. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration Nos. | Date of registration | Date of filing | Rightful institution | Remarks |
| Registration 52 | 10-598516 | 2005-35432 | Korea Institute of Industrial Technology | H05K 7/20 |
| Registration 52 | 2006.07.03 | 2005.04.28 | Korea Institute of Industrial Technology | H05K 7/20 |
| Registration 58 | 10-736810 | 2006-33109 | Korea Institute of Industrial Technology | G06F 1/20 |
| Registration 58 | 2007.07.02 | 2006.04.12 | Korea Institute of Industrial Technology | G06F 1/20 |
| Representative Figs. |

2. Summary of the technology

This technology relates to heat sink having heat pipe function, and method for manufacturing a heat sink having thermal siphon function.

In the conventional heat sink, heat is conducted from a heat source to a heat dissipating plate that is bottom surface of a heat sink, from the bottom surface of a heat sink to a heat dissipating fin, and then after the process, a heat dissipating fin is again contacted with the air, then the heat dissipating fin is cooled. In this manner, there has been a problem of a heat discharge limit, because the temperature differences between the end portion of a heat dissipating plate in a horizontal direction and the end portion of a heat dissipating fin in a vertical direction are too large, therefore the heat conduction amount relatively cannot but decreased itself.

This is the improved technology to overcome the afore said problem of a heat discharge limit, and is provided a devised heat sink having heat pipe function to remove temperature differences between a heat dissipating plate and a heat dissipating fin, therefore it provides the good heat conducting function through the air.

In this technology, a heat pipe unit formed in a heat dissipating fin is comprised of one of the following structures, for examples, a number of capillary grooves formed in a vertical direction to generate a capillary force in the hollow type inner wall of a heat dissipating fin, an inner wall formed with sintered metal, or a structure equipped with a mesh structure. This technology additionally comprises a mesh structure of porous or meshed form having large contact size in the inner portion as well as in a heat dissipating fin to increase the reaction rate of the dynamic fluids filled in a heat dissipating plate as to the heat source.

3. Characteristics and/or advantages of the technology

As a hollow type structure contacted with a heating element, this technology integrally forms a heat dissipating plate in a horizontal direction filled with dynamic fluids reacting rapidly to the heat source to thereby the vapors of the dynamic fluids is evaporated, and a number of hollow type heat dissipating fins in a vertical direction as to the afore said heat dissipating plate, wherein this technology characterized in that a heat pipe unit is equipped in an inner wall of the afore said heat dissipating fin to thereby vapors of the dynamic fluids reacting with the heat source of the heating element is evaporated and then is condensed by heat exchange with air through the heat dissipating fin and then is returned to the heat dissipating plate rapidly again, but the heat pipe unit formed in the afore said heat dissipating fin has a number of capillary grooves to generate a capillary force in the hollow type inner wall of the heat dissipating fin, and the afore said heat dissipating plate is composed of a mesh structure of porous or meshed form having large contact size in the inner portion as well as in the afore said heat dissipating fin to increase the reaction rate of the dynamic fluids as to the heat source.

This technology of the inner portion of the whole body formed to be hollow also features that not only the filled dynamic fluids react rapidly with the heat source of the heating element, but also the vapors of the dynamic fluids is evaporated and then is condensed by heat exchange with air and then is returned to the heat dissipating plate rapidly again by the capillary force. As a result, the temperature differences between a heat dissipating plate contacted with a radiating body and a heat dissipating fin exposed to the air are so slight, the protection against heat by heat transfer with the air can be dramatically improved.

4. Applicable market and use of the technology

This technology can be applicable to a large output power and long wavelength semiconductor laser, an electronic chip, an optical communication parts or an electronic parts, a condenser, and a PC like the electronic parts that needs to be cooled, which has large heat generating amount per the unit area as the high efficiency and high speed of working. This technology can be utilized by a small sized product because of its high heat generating amount per the unit area and especially can be applicable to all kinds of the electronic parts having heat generating problems.