APPARATUS AND METHOD FOR COMPOSING BEHAVIOR AND EXPRESSION OF HUMAN-LIKE ROBOT

1. Information of the patent

| Dowon International Administration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Application 47 | - | 2006-130633 | Korea Institute of Industrial Technology | B25J 13/00 |
| Application 47 | - | 2006.12.20 | Korea Institute of Industrial Technology | B25J 13/00 |
| Representative Fig. |

2. Summary of the technology

ㅇ 	This technology relates to an apparatus and method for composing behaviors and expressions of a human-like robot, which can express emotions, physiological reactions of a human, and lip synchronization through face expressions and body behaviors similar to a human.

ㅇ 	Conventional technologies disclose only a schematic structure of a robot, which has facial forms with respect to imaginary life not human faces and bodies and faces similar to a human when there is no main body and can understand human languages and express emotions through behaviors and expressions, but this technology is a technology regarding a method of controlling a motor so that the behaviors and expressions of a robot can be represented similar to a human.

ㅇ 	An apparatus for composing behaviors and expressions of a human-like robot includes a sensor module for receiving physical information of a real world from sensors mounted in a robot and converting the information into voltage that can be processed by the robot a recognition module for extracting necessary information from various pieces of information collected from the sensors; a scenario module for configuring user commands as a scenario and sequentially executing the commands; a task module for processing tasks classified according to unit behaviors; a behavior-based controller for selecting and executing adequate behaviors and expressions with respect to inputs of the sensors of the robot and outputs of an upper task; and a motor mediator for mediating contracting outputs when one or more behaviors are performed at the same time.

3. Characteristics and/or advantages of the technology

In basic behaviors of this technology, basic posture states of a main body include consecutively expressing sleep, doze and wake-up states.  In the wake-up state, a robot can take various postures.  Further, the face can have normal, joy, sadness, happiness, uneasiness states, etc. according to the states of emotions and several emotions can take place at the same time.  For example, in the case of a slight joy, normal 40% and joy 60% can be expressed at the same time.

Physiological reaction behaviors of this technology are characterized in that they can express reactions appearing as sympathetic nerve of a human body such as respiration, pulse, hiccup, yawning and eye flickering is activated, and an action container can express one or more intended and overlapping behaviors of a main body.  Further, an expression container is characterized in that it can express one or more intended and overlapping expressions of a face.

The motor mediator of this technology is characterized in that it produces contracting outputs which are produced when one or more behaviors are performed at the same time.

4. Applicable market and use of the technology

This technology can be applicable to robots that help a human life of robot fields and, therefore, can be used for robot fabrication companies, robot components, etc. and can be used in various fields employing robots.