INTELLIGENT TYPE HEALTH EQUIPMENT

1. Information of the patent

| Dowon International Administration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Application 91 | 10-784926 | 2005-53366 | Korea Institute of Industrial Technology | A63B 24/00 A63B 22/02 |
| Application 91 | 2007.12.05 | 2005.06.21 | Korea Institute of Industrial Technology | A63B 24/00 A63B 22/02 |
| Representative Fig. |

2. Summary of the technology

ㅇ	This technology relates to an intelligent exercise apparatus which can used by an exerciser who listens to audio(in particular, music) having time.

ㅇ	In general, while doing exercise, an exerciser listens to music having a rhythm suitable for an exercise speed(or an action cycle) or controls the exercise speed according to the music rhythm.  If an exerciser exercises with no music or a music rhythm does not coordinate with the exercise speed, the exerciser easily feels bored compared with a case where an exercise is performed with a sense of rhythm, thus reducing the exercise effects.  However, rhythms differ unless the same music is not repeated and times differ within the same song.  Thus, an exerciser controls the exercise speed every time when the time of music is changed.  This made the exerciser very inconvenient and there was a high possibility that safety accidents may occur since devices were controlled while exercising.

This technology is an improved technology regarding an intelligent exercise apparatus for measuring an exercise speed, more specifically, a repetitive action cycle of an exerciser, comparing the repetitive action cycle with rhythm(time) information of music, and when the exercise speed does not match the rhythm(time) information of music, changing the action cycle of the exerciser suitably for the time of the music or changing the time of the music suitably for the action cycle of the exerciser.

ㅇ	This technology is a technology regarding an intelligent exercise apparatus, including an exercise machine, a sensor unit for detecting an exercise speed(a repetitive action cycle) of an exerciser using the exercise machine; a music play unit for playing music of a specific time a time recognition unit for recognizing time played from the music play unit and a controller for comparing the repetitive action cycle of the exerciser input from the sensor unit with the time input from the music play unit, and changing the action cycle of the exerciser suitably for the time of the music or changing the time of the music suitably for the action cycle of the exerciser.

3. Characteristics and/or advantages of the technology

This technology is a technology regarding an intelligent exercise apparatus and is characterized in that it can change an action cycle of an exerciser suitably for time of music or changing the time of the music suitably for the action cycle of the exerciser.

This technology is advantageous in that it allows an exerciser to exercise under an optimal music environment and exercise environment and can enjoy exercise, and the amount of exercise is increased.

4. Applicable market and use of the technology

This technology can be applicable to an intelligent exercise apparatus in which an exercise machine, such as a running machine, a stepper or a health cycle, is coupled to an audio device so that an exerciser can listen to music while exercising.  Further, this technology can be applicable to a running machine apparatus in which a rotation speed(exercise speed) of a running machine is programmed to increase or decrease as an exercise time of an exerciser elapses and an apparatus for measuring the exercise speed of an exerciser and selecting and playing audio(music) of time suitably for a repetitive action cycle of the exerciser.