MASSAGE DEVICE COMPRISING ECCENTRIC UNIT; and MASSAGE DEVICE COMPRISING UNIT FOR INTERVAL REGULATION

1. Information of the patent

| Dowon International Administration Nos. | Registration Nos. | Application Nos. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration Nos. | Date of registration | Date of filing | Rightful institution | Remarks |
| Application 92 | 10-785097 | 2006-75926 | Korea Institute of Industrial Technology | A61H 7/00 |
| Application 92 | 2007.12.05 | 2006.08.11 | Korea Institute of Industrial Technology | A61H 7/00 |
| Application 93 | 10-786655 | 2006-75927 | Korea Institute of Industrial Technology | A61H 7/00 |
| Application 93 | 2007.12.11 | 2006.08.11 | Korea Institute of Industrial Technology | A61H 7/00 |
| Representative Figs. |

2. Summary of the technology

This technology relates to a mechanical massager having an eccentric unit or an interval adjusting device, thereby optimizing the massaging effects thereof.

In conventional practices, since a rotary shaft and a center shaft of a motor generating a rotary force of the rotary shaft are on the same line as each other, the motion radius of the massage pads coupled to the ends of massage members is reduced, such that the pressurizing effect of the massage pad applied to a human body can be decreased.  Further, the massage pads just hold the muscles of the human body, which reduces the massaging effects of the massager.  Moreover, in a state where the massage members coupled to the end portion of the rotary shaft are fixed by means of the structural shape of a cam member, the rotary shaft is rotated such that the opposing ends of the massage members are symmetrically opened and closed repeatedly, thereby carrying out the massaging operation.  In this case, the interval between the opposing ends of the massage members is not adjusted according to the regions of the human body or the muscles to be massaged, thereby failing to achieve satisfied massaging effects.

To the contrary, this technology provides a massager that can be applied appropriately to a desired region of the human body, and so as to improve the massaging effects, the massager further includes an eccentric unit or an interval adjusting device.

According to this technology, there is disclosed a massager having a rotary shaft rotated by means of a driving means, a hollow cam member fixedly coupled to the rotary shaft, a bearing coupled to one side surface of the cam member, a pair of massage members coupled to the outer periphery of the bearing in such a manner as to conduct opposing reciprocating movements by the rotation of the rotary shaft, and an eccentric unit having a given eccentric distance between the center of the driving shaft of the driving means and the center of the rotary shaft to which the massage members are coupled, the massager comprising: a rotary shaft rotated by means of a driving means; a cam member fixedly coupled to the rotary shaft to allow the left and right reciprocating motions of the ends of the massage members and having one side slanted; a bearing coupled to the slanted end surface of the cam member; a pair of massage members coupled to the outer periphery of the bearing in such a manner as to conduct left and right reciprocating movements by the rotation of the rotary shaft; and a ball screw part having a screw shaft coupled to one end of the hollow interior of the rotary shaft so as to adjust the interval between the pair of massage members coupled to the cam member, a nut member adapted to conduct left and right linear motions, while having lead screw motion by the rotation of the screw shaft, and a shaft supporting means coupled to one side of the screw shaft so as to support the screw shaft, thereby allowing the screw shaft to be rotated, the shaft supporting means having a screw bearing coupled to one side of the screw shaft, a fixing pad coupled to one side of the screw shaft so as to prevent escaping of the screw bearing, and a grip member coupled to the outside of the fixing pad so as to rotate the screw shaft.

3. Characteristics and/or advantages of the technology

This technology relates to a mechanical massager having the eccentric unit or the interval adjusting device, thereby optimizing the massaging effects thereof.

The massager according to this technology includes the eccentric unit having a given eccentric distance between the center of the driving shaft of the driving means and the center of the rotary shaft to which the massage members are coupled, thereby extending the motion radius of the massage members and conducting holding and pulling operations at the same time, which optimizes the massaging effects.

The massager according to this technology includes the interval adjusting device wherein the ball screw part is coupled inside the rotary shaft and as the ball screw part is rotated, the interval between the pair of massage members can be adjusted, thereby achieving more effective massaging operations in accordance with the regions to be massaged.

4. Applicable market and use of the technology

This technology relates to a massager and is applicable to a massager market.  There are presented various kinds of massagers in the market, such as a handy massager, a foot massager, a massage chair, a neck/shoulder massager, a belt type massager and so on.  The massager having the eccentric unit or the interval adjusting device according to this technology is applicable to the foot massager, the neck/shoulder massager, and the massage chair.