LIGHT MODULATOR

1. Information of the patent

| Dowon International dministration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International dministration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Registration 89 | 10-623521 | 2004-15918 | Korea Institute of Industrial Technology | G02F 1/01 |
| Registration 89 | 2006.09.06 | 2004.03.09 | Korea Institute of Industrial Technology | G02F 1/01 |
| Representative Fig. |

2. Summary of the technology

ㅇ 	This technology relates to a fabrication method which can easily implement a single, a number of and multiple diffraction gratings at the interface of a metal film and an electrooptic material film by employing a pattern mask.

ㅇ 	This technology has improved a disadvantage in that commercialization is difficult due to a slow response speed and problems in that an expensive high refraction prism must be used and miniaturization, high integration and mass-production of devices are difficult to realize due to a large prism.

ㅇ 	An optical modulation device of this technology includes a substrate; a single unit of a metal film stacked on the substrate; an electrooptic material film stacked on a top surface of the metal film; a micro diffraction grating formed at an interface of the metal film and the electrooptic material film; a transparent electrode stacked over the substrate and the electrooptic material film a power supply source connected to each of the metal film and the transparent electrode and an electrooptic polymer material constituting the electrooptic material film, wherein the electrooptic polymer material changes a surface plasmon resonance condition as the refractive index of the electrooptic material film is changed by the Pokels effect when voltage is applied to the metal film and the transparent electrode.

This technology can have an effect in that it can easily implement a single, a number of and multiple diffraction gratings at the interface of the metal film and the dielectric material by employing the pattern mask. Thus, this technology is characterized in that it can solve the problems of the existing method employing a high refractive prism and implement an optical modulation system employing micro diffraction grating-coupled surface plasmon resonance.

This technology is advantageous in that it can easily realize simplification, miniaturization, high integration and mass-production through a low fabrication cost when compared with the Kretschmann type surface plasmon optical modulator required by the existing high refractive prism.

3. Characteristics and/or advantages of the technology

This technology can have an effect in that it can easily implement a single, a number of and multiple diffraction gratings at the interface of the metal film and the dielectric material by employing the pattern mask. Thus, this technology is characterized in that it can solve the problems of the existing method employing a high refractive prism and implement an optical modulation system employing micro diffraction grating-coupled surface plasmon resonance.

This technology is advantageous in that it can easily realize simplification, miniaturization, high integration and mass-production through a low fabrication cost when compared with the Kretschmann type surface plasmon optical modulator required by the existing high refractive prism.

4. Applicable market and use of the technology

This technology can be applied to fabricate ultra-high speed optical switches, optical modulators, spatial-optical modulators, optical interconnects, optical filters, display and can also be largely applied to fabricate various components such as optical communication and information electronic fields.