OPTICAL FIBER LASER AT VISIBLE WAVELENGTH

1. Information of the patent

| Dowon International Administration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Registration 92 | 10-704603 | 2005-41253 | Korea Institute of Industrial Technology | H01S 3/067 |
| Registration 92 | 2007.04.02 | 2005.05.17 | Korea Institute of Industrial Technology | H01S 3/067 |
| Representative fig. |

2. Summary of the technology

This technology relates to a laser beam, and more particularly to a optical fiber laser beam at visible wavelength provided to generate optimum blue and green laser beam at the same time as a single semiconductor laser excitation light source, by using an Ytterbium-doped fiber and a Thorium-doped fiber.

A color display apparatus generates the three primary colors of red, green, and blue (R, G, B) by using the separate three light sources. The semiconductor laser light sources of green and blue, different from the semiconductor laser light source of red, are under research and development steps in the industrial usage aspect. Accordingly, as an alternative plan, research and development of a solid or optical fiber laser using a semiconductor laser as an excitation light is in progress.

In this circumstance, this technology can output blue and green laser beam by using an Ytterbium-doped fiber and a Thorium-doped fiber in the laser beam generating apparatus.

In addition, as a second optical fiber, it is possible to obtain a same result by using silica, zblan or chalcogenide fiber.

In a laser beam generating apparatus using a semiconductor laser generating a laser beam for pumping and a lens collecting the pumping light generated from the semiconductor laser, this technology is comprised of an Ytterbium-doped optical fiber, which makes laser oscillation by stimulated emission by an input light and emits a light by up-conversion of the laser beam of the semiconductor laser; and a second optical fiber, which receives the light outputted from the Ytterbium-doped optical fiber and not-absorbed semiconductor laser beam, and emits a prescribed light by up-conversion of the incident infrared laser beam.

3. Characteristics and/or advantages of the technology

This technology characterized in that a optical fiber laser at visible wavelength is provided to generate optimum blue and green laser beam at the same time as a semiconductor laser excitation light source, by using an Ytterbium-doped fiber and a thorium-doped fiber.

In addition, this technology features that it is possible to output the optimum laser beam of blue and green, by using Silica, Zblan, or Chalcogenide fiber.

4. Applicable market and use of the technology

This technology can be applicable to a field of an image analysis of optical microscope for metal, semiconductor, biology, and medical science, a field of public machinery center or analysis room to manage images with central concentration method by transmitting and sharing the images of an image apparatus to network or by using file server (option); and a field of managing or inputting the picture, slide, and so on easily.

With respect to the application of this technology, it is possible to accomplish more strengthen image software, whose main purpose is acquiring image; to store/ manage/ output/ search the images acquired from an optical microscope; to constitute of network system that is suitable to user's circumstance and share image material; to measure length, area, and so on by an image, and measure and analyze corpuscular factor, and so on; to manage organized image data, and provide user's convenience-centered program managing environment.

Accordingly, the use of this technology makes possible of shorter work time, raised business efficiency, lowered cost. And also, anyone can use this technology conveniently, and the technology can support many kinds of image editing or making reports, and correct and detailed analysis via automation of image measurement/ measuring.