METHOD FOR IMPROVING ANAEROBIC DIGESTION TREATMENT EFFICIENCY OF WASTE ACTIVATED SLUDGE

1. Information of the patent

| Dowon International Administration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Registration 16 | 10-489696 | 2003-21848 | Korea Institute of Industrial Technology | C02F 11/04 |
| Registration 16 | 2005.05.04 | 2003.04.08 | Korea Institute of Industrial Technology | C02F 11/04 |
| Representative Fig. |

2. Summary of the technology

ㅇ	This technology relates to a method for pre-processing a waste activated sludge before applying an anaerobic digestion process to the waste activated sludge.

ㅇ	Whereas active researches have been conducted on technologies for using waste activated sludges(biomass) through gasification under the leadership of government and national research laboratories in foreign countries,  domestic researches remain in elementary levels due to economy, reclaimed land security, and sludge wet in terms of alternative energy and have not yet been commercialized.  Although biomass does not exhaust carbon dioxide that is a main cause for global warming and has high utilization value for use as a substitute for fossil fuel, it has a disadvantage of long reaction(fermentation) time.

On the other hand, this technology not only can process organic waste efficiently, but also can be recycled as a high-additional value fuel.  Moreover, the efficiency in decomposition and fermentation is improved by various pre-processing processes and processing time and contamination load can be reduced efficiently.

ㅇ	A method for improving the anaerobic digest processing efficiency of a waste activated sludge according to this technology performs a pre-processing step selected from among thermal pre-processing, chemical pre-processing, ultrasonic wave pre-processing, and thermal-chemical pre-processing.

3. Characteristics and/or advantages of the technology

This technology reduces decomposition time and improving generation of methane gas, and efficiently reducing contamination load by pre-processing a waste activated sludge before putting the waste activated sludge into an aerobic digest process.

By performing a pre-processing step according to this technology, the size of a grain can be reduced by about 45~65 % and volatile solid matters and available chemical oxygen demand(SCOD) are also reduced by 47~130 %, thereby reducing processing time and contamination load efficiently.  Moreover, the amount of bio-gas and methane gas generated increases by about 34.3 %.

4. Applicable market and use of the technology

This technology relates to a method for processing a waste activated sludge and its applicable market is the field of sewage/waste water processing.  Since an aerobic digest process is used to process a large amount of waste activated sludge generated during sewage/waste water processing, this technology can be used in large-scale factories or apartment complexes having a large amount of sewage/waste water and sludges generated and other facilities for processing sewage/waste water.

Since a large amount of bio-gas and methane gas generated after sewage/waste water processing can also be recycled as an energy source, this technology is environment-friendly.