STEREO VISION APPARATUS FOR SEARCHING AND RECOGNIZING AN OBJECT FOR A ROBOT AND A CONTROL METHOD THEREOF

1. Information of the patent

| Dowon International Administration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Registration 83 | 10-638567 | 2005-23927 | Korea Institute of Industrial Technology | B25J 5/00 G06F 17/30 G06F 17/00 |
| Registration 83 | 2006.10.19 | 2005.03.23 | Korea Institute of Industrial Technology | B25J 5/00 G06F 17/30 G06F 17/00 |
| Representative fig. |

2. Summary of the technology

This technology relates to a stereo vision apparatus for searching and recognizing an object for a robot and a control method thereof.

A camera using method for searching and recognizing an object has been taken long times for processing data of a large amount of arithmetic because the method has to know the information of an object ahead of time or has to acquire the information in real-time. It seems like the method provide the information with high reliability in a restricted environment, however, in an opposite case, it has been a problem in that the method provides unreliable information. And, it also has problems that one vision camera recognizing an object installed in a mobile robot not only doesn't recognize a moving object, but it is also difficult for one vision camera to measure the distance data exactly.

This is the improved technology to overcome the aforesaid problems of a vision camera, and is provided to more reliability for searching and recognizing an object for a robot by control of stereo vision using active tag and IRED(Infrared Emitting Diode).

This technology of a stereo vision apparatus for searching and recognizing an object for a robot comprises an active tag equipped with the IRED(InfraRed Emitting Diode); a robot containing a communication unit sending a blinking signal a stereo vision recognizing an object and a control apparatus recognizing an object after control the stereo vision, regulating the pan(a right and left rotary motion)-tilt(an up and down rotary motion), and measuring the distance of active tag and stereo vision by extracting the mutual relation between a robot and an object with the variation of an angle. The apparatus measure the distance, and confirms the location.

3. Characteristics and/or advantages of the technology

This technology characterized in that a stereo vision apparatus for searching and recognizing an object for a robot comprises an active tag attached to the object and equipped with the IRED(InfraRed Emitting Diode), a robot recognizing the aforesaid active tag and containing a communication unit sending a blinking signal to the IRED after connecting with the active tag, a stereo vision sensing the IRED blinked by the communication unit of the robot and recognizing the object, and a control apparatus sensing the flickering IRED, controlling the stereo vision to guide the IRED to come to the center by regulating the pan-tilt, comparing an image when the IRED is on and an image when the IRED is off, and extracting the mutual relation. The stereo vision apparatus senses the difference between the image when the IRED is on and the image when the IRED is off and recognizes the object, measures the distance, and confirms the location.

This technology provide more reliable result than the conventional vision processing method because of using the active tag, and makes possible to trace an object's movement more easily by the pan-tilt function. It also has an advantage of applicability to a mobile robot.

4. Applicable market and use of the technology

This technology, as an applicable technology to a various field, it is possible to utilizing a stereo remote-system or an adaptable pattern recognizing system by using a stereo vision system, for utilizing the feature of real-time character pattern and the features of various objects.

In addition, the remote medical treatment or education system using a stereo vision and providing the real recognizing environment of human narrows the gap caused by the spatial isolation and provides the opportunity of virtual education. The three-dimensional remote medical system basis on the stereo vision can transmit and estimate medical images and a patient's images in real-time for doctors without the inconvenience of time and places to thereby provide high quality medical service. And besides, this technology can be applicable to a various fields, for examples, a tracing of a target by using information of a time difference and pixel similarity, a system of sensing obstacle for a automatic return vehicle, a supplement of robot, a motor car, and a semiconductor examination.