Title of Invention

Vegetation base for greening rooftop, vegetation mat having vegetation base and method for manufacturing the vegetation mat

| Ⅰ |  | Analysis of Technical Trend |
| --- | --- | --- |

1. Summary of Technology

| Definition |  | The present invention relates to a method for manufacturing lightweight vegetation base and mat. The vegetation base of the present invention includes a plurality of closely formed wood chips and a plurality of fillers adapted to be filled into the spaces between the plurality of wood chips so as to maintain the closely formed wood chips to a plate-like shape. |
| --- | --- | --- |
|  |  | The present invention relates to a method for manufacturing lightweight vegetation base and mat. The vegetation base of the present invention includes a plurality of closely formed wood chips and a plurality of fillers adapted to be filled into the spaces between the plurality of wood chips so as to maintain the closely formed wood chips to a plate-like shape. |
| Keyword |  | greening for rooftop, vegetation base, vegetation mat, vegetation base for greening rooftop, method for manufacturing vegetation mat |
|  |  | greening for rooftop, vegetation base, vegetation mat, vegetation base for greening rooftop, method for manufacturing vegetation mat |
| Related Figure |  |  |  |
| Technical Characteristics & Merit |  | a) The vegetation base of the present invention is simply applied for various vegetation, without needing any growing soil such as general soil, artificial soil and the like, and since it is light in weight, the vegetation base is very useful in the greening of the rooftop of a building. b) The vegetation base and the vegetation mat of the present invention is simply placed on an artificial ground irrespective of their construction place, thereby accomplishing artificial greening. c) The vegetation mat includes a vegetation layer on which seeding is conducted and a vegetation layer adapted to grow the seeds, which are separably formed from each other, such that the seeds selected according to the preferences of users are planted and the construction of the vegetation mat is achieved in a very simple way. |
|  |  | a) The vegetation base of the present invention is simply applied for various vegetation, without needing any growing soil such as general soil, artificial soil and the like, and since it is light in weight, the vegetation base is very useful in the greening of the rooftop of a building. b) The vegetation base and the vegetation mat of the present invention is simply placed on an artificial ground irrespective of their construction place, thereby accomplishing artificial greening. c) The vegetation mat includes a vegetation layer on which seeding is conducted and a vegetation layer adapted to grow the seeds, which are separably formed from each other, such that the seeds selected according to the preferences of users are planted and the construction of the vegetation mat is achieved in a very simple way. |

2. Present Status of Intellectual Property

| Country | Right | Status | Application No. (Filing Date) | Registration No. (Registration Date) |
| --- | --- | --- | --- | --- |
| Korea | patent | registered | 10-2007-056581 (2007.06.11) | 10-0828167 (2008.04.30) |
| Title of Invention | Vegetation base for greening rooftop, vegetation mat including vegetation base, and method for manufacturing vegetation mat |

| Ⅱ |  | Analysis of Market Trend |
| --- | --- | --- |

1. Summary of Applicable Market

| Summary of Industry |  | The greening of rooftop solves the problem from the ecological view of a city and at the same time achieves energy saving by utilizing the rooftop space which is not managed in the city in a range from a small-sized private space to a large-sized public space, thereby upgrading the value of the environment-friendly living space. Recently, with the development of the study on the greening of rooftop, the studies on the structure of the rooftop greening system and the constructability thereof with more developed technology have been definitely needed. |
| --- | --- | --- |
|  |  | The greening of rooftop solves the problem from the ecological view of a city and at the same time achieves energy saving by utilizing the rooftop space which is not managed in the city in a range from a small-sized private space to a large-sized public space, thereby upgrading the value of the environment-friendly living space. Recently, with the development of the study on the greening of rooftop, the studies on the structure of the rooftop greening system and the constructability thereof with more developed technology have been definitely needed. |
| Definition and Scope of Market |  | The vegetation base and the vegetation mat according to the present invention are applied to the products accomplishing the artificial greening, without any limitation of the construction place. |
|  |  | The vegetation base and the vegetation mat according to the present invention are applied to the products accomplishing the artificial greening, without any limitation of the construction place. |

2.  Characteristics of Market

| Market Scale |  | In the market of the rooftop greening, the rooftop greening area of about 200km2 exists in the existing buildings in Seoul city, and the market of the rooftop greening has a potentiality in a range of 20 to 30 trillion won. Seoul city invested 2.8 billion won till 2006 and further will invest 13 billion won by 2010, so as to support the rooftop greening business. |
| --- | --- | --- |
|  |  | In the market of the rooftop greening, the rooftop greening area of about 200km2 exists in the existing buildings in Seoul city, and the market of the rooftop greening has a potentiality in a range of 20 to 30 trillion won. Seoul city invested 2.8 billion won till 2006 and further will invest 13 billion won by 2010, so as to support the rooftop greening business. |
| Market Trend |  | Even if the rooftop greening business in Korea starts more late when compared with other countries, the interest is relatively high, and recently, the construction cases are increased. Seoul supports the rooftop greening business on 46 places including Korea UNESCO center from 2002 and performs the rooftop greening of the area of 17,680m2. The rooftop greening is expanded to Seoul 100,000 green roof-making business in 2007, which enters full scale step. In the era of high oil prices, each of provinces staying at an initial step in the rooftop greening business makes green space foundations by which the rooftop greening business is carried out dynamically. Especially, Ulsan and Daegu have developed the rooftop greening business for apartments, stores, public buildings and the like. |
|  |  | Even if the rooftop greening business in Korea starts more late when compared with other countries, the interest is relatively high, and recently, the construction cases are increased. Seoul supports the rooftop greening business on 46 places including Korea UNESCO center from 2002 and performs the rooftop greening of the area of 17,680m2. The rooftop greening is expanded to Seoul 100,000 green roof-making business in 2007, which enters full scale step. In the era of high oil prices, each of provinces staying at an initial step in the rooftop greening business makes green space foundations by which the rooftop greening business is carried out dynamically. Especially, Ulsan and Daegu have developed the rooftop greening business for apartments, stores, public buildings and the like. |