Title of Invention

Integrated environment monitoring system

| Ⅰ |  | Analysis of Technical Trend |
| --- | --- | --- |

1. Summary of Technology

| Definition |  | The present invention relates to an automatic remote monitoring system that is installed at mountainous area so as to monitor forest fire and environment, and more particularly, to an integrated environment monitoring system that is installed at the peak of a mountain and includes a main monitoring part for sensing the occurrence of specific situations at the area within a radius in a range between 4km and 12km through the comparison and analysis of the data obtained from various sensors and camera images and a plurality of auxiliary monitoring parts installed at the corners of the area monitored by the main monitoring part for assisting the main monitoring part, thereby monitoring the situation of forest fire and all kinds of environments in the corresponding mountainous area. |
| --- | --- | --- |
|  |  | The present invention relates to an automatic remote monitoring system that is installed at mountainous area so as to monitor forest fire and environment, and more particularly, to an integrated environment monitoring system that is installed at the peak of a mountain and includes a main monitoring part for sensing the occurrence of specific situations at the area within a radius in a range between 4km and 12km through the comparison and analysis of the data obtained from various sensors and camera images and a plurality of auxiliary monitoring parts installed at the corners of the area monitored by the main monitoring part for assisting the main monitoring part, thereby monitoring the situation of forest fire and all kinds of environments in the corresponding mountainous area. |
| Keyword |  | forest fire, monitoring, environment |
|  |  | forest fire, monitoring, environment |
| Related Figure |  |  |  |
| Technical Characteristics & Merit |  | a) Using the integrated environment monitoring system according to the present invention, a predetermined area to which monitoring is required is selected and carefully monitored and managed. b) The object and conditions to be monitored are directly controlled by a situation room according to situations, and once installed, the monitoring parts are used for various purposes. c) The main monitoring part monitoring a wide area is constructed at high prices and the auxiliary monitoring parts monitoring a local area is constructed at low prices, thereby saving the installing and managing costs of the system. |
|  |  | a) Using the integrated environment monitoring system according to the present invention, a predetermined area to which monitoring is required is selected and carefully monitored and managed. b) The object and conditions to be monitored are directly controlled by a situation room according to situations, and once installed, the monitoring parts are used for various purposes. c) The main monitoring part monitoring a wide area is constructed at high prices and the auxiliary monitoring parts monitoring a local area is constructed at low prices, thereby saving the installing and managing costs of the system. |

2. Present Status of Intellectual Property

| Country | Right | Status | Application No. (Filing Date) | Registration No. (Registration Date) |
| --- | --- | --- | --- | --- |
| Korea | patent | registered | 10-2001-0062334 (2001.10.10) | 10-0452118-0000 (2004.09.30) |
| Title of Invention | Integrated environment monitoring system |

| Ⅱ |  | Analysis of Market Trend |
| --- | --- | --- |

1. Summary of Applicable Market

| Summary of Industry |  | With the rapid economic growth and the drastic increase of the national land development and utilization, the damage of natural environment and the destruction of ecosystem become more and more severe. Accordingly, the importance of the preservation of the natural environment is emphasized such that natural environment preservation plan is totally revised on Dec. 1997, and based upon the same plan, the whole country natural environment preservation plan is built every five years. Moreover, natural ecosystem preservation, wild animal/plant protection, and natural environment protection are carried out through the related departments, and the discussion on the whole country natural environment preservation plan is made through cities and provinces, which exhibits the interest of the government in the natural environment preservation. |
| --- | --- | --- |
|  |  | With the rapid economic growth and the drastic increase of the national land development and utilization, the damage of natural environment and the destruction of ecosystem become more and more severe. Accordingly, the importance of the preservation of the natural environment is emphasized such that natural environment preservation plan is totally revised on Dec. 1997, and based upon the same plan, the whole country natural environment preservation plan is built every five years. Moreover, natural ecosystem preservation, wild animal/plant protection, and natural environment protection are carried out through the related departments, and the discussion on the whole country natural environment preservation plan is made through cities and provinces, which exhibits the interest of the government in the natural environment preservation. |
| Definition and Scope of Market |  | The object of the present invention is to provide an integrated environment monitoring system that transmits only the situation difficult to determine or being at a serious state to a system of a situation room to receive the immediate determination and action from the situation room, thereby performing the monitoring of forest fire and environment. |
|  |  | The object of the present invention is to provide an integrated environment monitoring system that transmits only the situation difficult to determine or being at a serious state to a system of a situation room to receive the immediate determination and action from the situation room, thereby performing the monitoring of forest fire and environment. |

2.  Characteristics of Market

| Market Scale |  | Referring to the situations and features of the drafting of the forest budget of 1.4268 trillion won in 2007, the budget of 38.94 billion won is drafted in the forest resource promotion field for the execution of the various functions of forest and the job creation, which is more increased by 1.4% when compared with that in 2006. Further, the budget of 28.06 billion won is drafted for the forest disaster prevention, which is more increased by 11.6% when compared with the budget of 25.14 billion won in 2006. Also, annual 500 erosion control dam facilities which provide high flood prevention effects will be installed according to the whole of government flood prevention plan, and in addition, the budget (400 million won) for the construction of the places spaced from wooden buildings for protecting the wooden buildings like natural forest resorts and temples in the forest and the budget (2.6 billion won) for the construction of fire prevention facility of forest resorts are newly drafted. |
| --- | --- | --- |
|  |  | Referring to the situations and features of the drafting of the forest budget of 1.4268 trillion won in 2007, the budget of 38.94 billion won is drafted in the forest resource promotion field for the execution of the various functions of forest and the job creation, which is more increased by 1.4% when compared with that in 2006. Further, the budget of 28.06 billion won is drafted for the forest disaster prevention, which is more increased by 11.6% when compared with the budget of 25.14 billion won in 2006. Also, annual 500 erosion control dam facilities which provide high flood prevention effects will be installed according to the whole of government flood prevention plan, and in addition, the budget (400 million won) for the construction of the places spaced from wooden buildings for protecting the wooden buildings like natural forest resorts and temples in the forest and the budget (2.6 billion won) for the construction of fire prevention facility of forest resorts are newly drafted. |
| Market Trend |  | Forest service starts to perform various forest fire prevention activities through the mountain-entering control up to 50% of the whole forests according to the forest fire danger prediction during the danger period of the forest fire and the closing of mountaineering path. Further, the forest fire danger causes are previously removed by burning the ridges between fields in a unit of small villages, and the individual burning is strictly controlled. Also, previous prediction type mobile control activities are strengthened for the main mountaineering path entrances and the crowded areas of the forests. According to the future plan of the forest service, the whole country is divided into two sections for rapidly finding the existence of fire, and the light airplanes for monitoring forest fire always fly to perform the aerial monitoring. Also, 191 forest fire automatic monitoring cameras are operated to perform ground monitoring. If the environment monitoring system of the present invention is applied to the various activities made by the forest service, the forest fire prevention will be more effectively achieved. |
|  |  | Forest service starts to perform various forest fire prevention activities through the mountain-entering control up to 50% of the whole forests according to the forest fire danger prediction during the danger period of the forest fire and the closing of mountaineering path. Further, the forest fire danger causes are previously removed by burning the ridges between fields in a unit of small villages, and the individual burning is strictly controlled. Also, previous prediction type mobile control activities are strengthened for the main mountaineering path entrances and the crowded areas of the forests. According to the future plan of the forest service, the whole country is divided into two sections for rapidly finding the existence of fire, and the light airplanes for monitoring forest fire always fly to perform the aerial monitoring. Also, 191 forest fire automatic monitoring cameras are operated to perform ground monitoring. If the environment monitoring system of the present invention is applied to the various activities made by the forest service, the forest fire prevention will be more effectively achieved. |