21. PCM manufacturing apparatus

| Ⅰ |  | Analysis of Technical Trend |
| --- | --- | --- |

1. Summary of Technology

| Definition |  | The present invention relates to a PCM manufacturing apparatus, which includes: a PCM supply tank having a supply valve for supplying PCM to the outside and stirring means for stirring the inside PCM to be uniformized; a PCM storage tank having a supply pipe for supplying PCM to the PCM supply tank, a turnaround input pipe for a feedback of the PCM from the PCM tank, and stirring means for stirring PCM to be uniformized; and a cooler for supplying refrigerant to heat-exchanging means mounted inside the PCM storage tank and supplying cold heat to the PCM. |
| --- | --- | --- |
|  |  | The present invention relates to a PCM manufacturing apparatus, which includes: a PCM supply tank having a supply valve for supplying PCM to the outside and stirring means for stirring the inside PCM to be uniformized; a PCM storage tank having a supply pipe for supplying PCM to the PCM supply tank, a turnaround input pipe for a feedback of the PCM from the PCM tank, and stirring means for stirring PCM to be uniformized; and a cooler for supplying refrigerant to heat-exchanging means mounted inside the PCM storage tank and supplying cold heat to the PCM. |
| Keyword |  | PCM, PCM manufacturing apparatus |
|  |  | PCM, PCM manufacturing apparatus |
| Related Figure |  |  | <Representative drawing> Schematic diagram of a PCM manufacturing apparatus according to a preferred embodiment of the present invention |
|  |  |  | <Representative drawing> Schematic diagram of a PCM manufacturing apparatus according to a preferred embodiment of the present invention |
| Technical Characteristics & Merit |  | ① The present invention can uniformize weight of PCM by rapidly cooling PCM to a wanted temperature and preventing a precipitation phenomenon, and accumulate cold by recovering the used PCM. ② The present invention can always supply PCM of a fixed temperature. |
|  |  | ① The present invention can uniformize weight of PCM by rapidly cooling PCM to a wanted temperature and preventing a precipitation phenomenon, and accumulate cold by recovering the used PCM. ② The present invention can always supply PCM of a fixed temperature. |

2. Present Status of Intellectual Property

| Country | Right | Status | Application No. (Filing Date) | Registration No. (Registration Date) |
| --- | --- | --- | --- | --- |
| Korea | Patent | Registered | 10-2006-0040163 (2006.05.03) | 10-0758248-0000 (2007.09.06) |
| Title of Invention | PCM manufacturing apparatus |

| Ⅱ |  | Analysis of Market Trend |
| --- | --- | --- |

1. Summary of Applicable Market

| Summary of Industry |  | The food supplies distribution industry is developing in a direction to manage a mass purchase and a service for rapidly supplying fresh and clean food materials through a renovation of a distribution structure. In 2007, the food business circles were shaken greatly because of problems of safety and relief of foods. Accordingly, the food service industry and franchise companies concentrate their energies on indication of the original home, upgrade and distribution of food materials. |
| --- | --- | --- |
|  |  | The food supplies distribution industry is developing in a direction to manage a mass purchase and a service for rapidly supplying fresh and clean food materials through a renovation of a distribution structure. In 2007, the food business circles were shaken greatly because of problems of safety and relief of foods. Accordingly, the food service industry and franchise companies concentrate their energies on indication of the original home, upgrade and distribution of food materials. |
| Definition and Scope of Market |  | The present invention relates to a PCM manufacturing apparatus, which can uniformize weight of PCM by rapidly cooling PCM to a wanted temperature and preventing a precipitation phenomenon, and accumulate cold by recovering the used PCM, and is applicable to the food materials distribution industry. |
|  |  | The present invention relates to a PCM manufacturing apparatus, which can uniformize weight of PCM by rapidly cooling PCM to a wanted temperature and preventing a precipitation phenomenon, and accumulate cold by recovering the used PCM, and is applicable to the food materials distribution industry. |

2. Characteristics of Market

| Market Scale |  | It is presumed that the scale of food material market including meal services and food services reaches KR￦13,000,000,000,000won in 2006, and the meal services out of the food material market occupies KR￦3,000,000,000,000won. Especially, large-scale meal service companies, in which the number of meals a day exceeds a hundred thousand, expand a business range based on their own infra structure since they are equipped with a sufficient infra in the food material business. According to a social trend, such as an increase of GDP, a spread of the five-day working system, an increase of an eating-out rate due to the entry of women in public affairs, an increase of large-scale foo service companies, an increase of outsourcing of food material delivery, and so on, it is presumed that the food material distribution market in korea reaches a scale of from KR￦19,000,000,000,000won to KR￦20,000,000,000,000won as of 2008. |
| --- | --- | --- |
|  |  | It is presumed that the scale of food material market including meal services and food services reaches KR￦13,000,000,000,000won in 2006, and the meal services out of the food material market occupies KR￦3,000,000,000,000won. Especially, large-scale meal service companies, in which the number of meals a day exceeds a hundred thousand, expand a business range based on their own infra structure since they are equipped with a sufficient infra in the food material business. According to a social trend, such as an increase of GDP, a spread of the five-day working system, an increase of an eating-out rate due to the entry of women in public affairs, an increase of large-scale foo service companies, an increase of outsourcing of food material delivery, and so on, it is presumed that the food material distribution market in korea reaches a scale of from KR￦19,000,000,000,000won to KR￦20,000,000,000,000won as of 2008. |
| Market Trend |  | It is dominantly analyzed that the food material distribution market was just beginning to be formed due to a retarded distribution structure, a flood of middle-sized small-scale businessmen, and absence of a formalized distribution model in spite of the market scale reaching about ￦10,000,000,000,000won. Accordingly, it is expected that competition among companies, which are equipped with various distribution infra structures, for the food material market, which is not yet opened, will be keen. |
|  |  | It is dominantly analyzed that the food material distribution market was just beginning to be formed due to a retarded distribution structure, a flood of middle-sized small-scale businessmen, and absence of a formalized distribution model in spite of the market scale reaching about ￦10,000,000,000,000won. Accordingly, it is expected that competition among companies, which are equipped with various distribution infra structures, for the food material market, which is not yet opened, will be keen. |