ULTRASONIC BONDING DEVICE

1. Information of the patent

| Dowon International Administration Nos. | Registration Nos. | Application Nos. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration Nos. | Date of registration | Date of filing | Rightful institution | Remarks |
| Application 98 | - | 2007-9180 | Korea Institute of Industrial Technology | H01M2/00 |
| Application 98 | - | 2007.01.30 | Korea Institute of Industrial Technology | H01M2/00 |
| Application 99 | - | 2007-9181 | Korea Institute of Industrial Technology | H01M2/00 |
| Application 99 | - | 2007.01.30 | Korea Institute of Industrial Technology | H01M2/00 |
| Application 100 | - | 2007-9183 | Korea Institute of Industrial Technology | H01M2/00 |
| Application 100 | - | 2007.01.30 | Korea Institute of Industrial Technology | H01M2/00 |
| Representative Figs. |

2. Summary of the technology

ㅇ This technology relates to a device for binding chemical fiber whole cloth by using ultrasonic bonding, which can be effectively used to sew long and three-dimensional parts such as seams, sleeve hems, slacks holes, and sleeve breadths of clothes.

ㅇ This technology improves problems of conventional technologies that puckering occurs around seams of stitched lines when each combination is not completely matched due to feed dogs, pressures of pressure feet, sewing thread tension, and cloth types, and in particular, difficulties in seam-sealing tasks on the puckered part may result in inferior goods, causing productivity degradation.

ㅇ This technology provides a device for sewing and bonding chemical fiber clothes by using ultrasonic bonding, the device including a frame constituting a supporting structure; a cloth pressurizing unit for pressurizing a plurality of sewing clothes supplied onto the frame; a cloth supporting unit having a supporting lever protruding to the left and to the right orthogonally to the cloth moving direction at an intermediate side of the frame and having a pattern roller supporting the sewing clothes inside the supporting lever; an ultrasonic generating unit having a tool horn disposed opposite to a pressurizing roller or disposed on the pattern roller in order to deliver ultrasonic waves to the sewing clothes and to melt-bond the overlapping portion of the clothes; a height adjusting unit having a driving cylinder for lifting or lowering the cloth pressurizing unit in order to adjust the pressurizing force of the roller; a cloth outlet unit having a driving roller and a supporting roller for drawing out the sewn clothes passing through the pressurizing roller of the cloth pressurizing unit and the tool horn of the ultrasonic generating unit; and a foot step unit having switches for delivering a driving force to the pressurizing roller of the cloth pressuring unit and the driving roller of the cloth outlet unit, actuating the tool horn of the ultrasonic generating unit, and actuating the driving cylinder of the height adjusting unit.

3. Characteristics and/or advantages of the technology

This technology can completely solve a problem that seam puckering caused by ultrasonic bonding results in defectiveness of a sewing process during sewing of chemical fiber clothes used for safety protective clothing, and thus  can accomplish a high-quality sewing task having complete sealing in seam portions, thereby remarkably improving sewing productivity while reducing the weight of labor costs.

4. Applicable market and use of the technology

This technology relates to an ultrasonic bonding device used for sewing of chemical fiber clothes, which can be applied to various fields such as bonding of thermoplastic plastic, plastic films, and synthetic fibers as well as manufacturing of special clothing like safety protective clothing.