ULTRASONIC MOTOR

1. Information of the patent

| Dowon International Administration No. | Registration No. | Application No. | Rightful institution | Remarks |
| --- | --- | --- | --- | --- |
| Dowon International Administration No. | Date of registration | Date of filing | Rightful institution | Remarks |
| Application 54 | - | 2006-40903 | Korea Institute of Industrial Technology | H02N 2/04 |
| Application 54 | - | 2006.05.08 | Korea Institute of Industrial Technology | H02N 2/04 |
| Representative Fig. |

2. Summary of the technology

This technology relates to an ultrasonic motor that conducts only up and down movements in horizontal vibration applied to an object to be driven, while having no vertical vibration components, and that is fixed at a plurality of points, thereby increasing the stiffness for a stable supporting structure.

As the conventional ultrasonic motors have an one-point supporting structure relative to a flange part, thereby making it difficult to ensure the stiffness for the support portion, and further, the unbalance of oval track is caused from the both side pressing tips according to the horizontal vibration, thereby making it difficult to achieve normal driving.

This technology ensures the normal driving, increases the stiffness for a stable supporting structure by means of the fixing at a plurality of points, and provides an integrated single vibration body such that the manufacturing is easy and the durability is increased.

According to this technology, there is disclosed an ultrasonic motor comprising: a body; first and second ultrasonic vibration means located sequentially at the both sides from the center of the body so as to vibrate the body in vertical and horizontal directions; an extension part having three or more joints at which the vertical and horizontal vibration correspond to each other and having corresponding bellies formed between the corresponding joints, so as to extend the length of the body; a plurality of fixing means mounted at the joints corresponding to each other in the body or/and the extension part; and a plurality of pressing tips mounted at the bellies corresponding to each other in the body or/and the extension part.

3. Characteristics and/or advantages of the technology

This technology relates to the ultrasonic motor using the vibration of the piezoelectric element by means of high frequency current, and more particularly, to the ultrasonic motor that conducts only up and down movements in horizontal vibration applied to an object to be driven, while having no vertical vibration components.

According to this technology, as the motor is fixed at the plurality of points, the stiffness for a stable supporting structure can be increased, and as an integrated single vibration body is provided, the manufacturing is easy and the durability is increased.

4. Applicable market and use of the technology

This technology is applicable to a means for driving a small object like a zoom mechanism in a camera.

Recently, the utilization of this technology is increasingly enlarged when the motor is adopted as a driving means on a stage used during positioning or returning process in a precise machining device, a measuring device or an exposing device, a checking device and an analyzing device used in the semiconductor manufacturing process.